## Slide 1
DIGITAL DESIGN • MINI PROJECT
8-BIT PISO
SHIFT REGISTER
Parallel-In Serial-Out (PISO)
Design • Working • Logisim Demo • Applications
Name: __________________ | Roll No.: __________________
1
0
1
1
0
0
1
0
LOAD → SHIFT → SERIAL OUT

## Slide 2
1. Problem Statement
What problem does a PISO register solve?
02
THE CHALLENGE
How can 8 bits of data be loaded at the same time, then sent out one bit at a time?
Parallel input: all 8 bits enter together.
Serial output: one bit is transmitted on each clock pulse.
The circuit should support loading and shifting in a controlled way.
INPUT: 8 BITS AT ONCE
1
0
1
1
0
0
1
0
SHIFT REGISTER
1
0
1
1
0
0
1
0
SERIAL OUTPUT: 1 BIT / CLOCK
Goal: demonstrate the load and shift modes in Logisim and verify the output sequence.

## Slide 3
2. Design / Methodology
Conceptual schematic — editable PowerPoint shapes, designed to recreate in Logisim
03
DESIGN FLOW
1
Choose 8-bit input
2
Load all bits in parallel
3
Apply clock pulses
4
Read serial output
8-STAGE REGISTER (SIMPLIFIED LOGISIM-STYLE VIEW)
Parallel inputs
D0
FF
Q0
D1
FF
Q1
D2
FF
Q2
D3
FF
Q3
D4
FF
Q4
D5
FF
Q5
D6
FF
Q6
D7
FF
Q7
CLK
Serial out
LOAD mode: capture D7–D0 together | SHIFT mode: move data one stage per clock
Implementation note: use 8 D flip-flops (or a shift-register component), a clock, and a load/shift control. Exact pin setup depends on the Logisim version.

## Slide 4
3. Demo in Logisim
Suggested live demonstration sequence
04
BUILD & TEST
01
Place 8 D flip-flops / an 8-bit register.
02
Add 8 input pins, a clock, and a serial output pin.
03
Wire the parallel inputs and shift path.
04
Load a test byte, e.g. 10110010.
05
Pulse the clock and record each serial bit.
ILLUSTRATIVE OUTPUT TRACE
LOAD
10110010
CLK 1
1011001•
CLK 2
101100••
CLK 3
10110•••
CLK 4
1011••••
Capture the actual Logisim screen here after testing.
Note: the trace is illustrative. Confirm shift direction and output order in your chosen circuit before presenting.

## Slide 5
4. Working & Applications
How data moves through the register
05
1 LOAD
Set LOAD mode and place 8-bit data on the input pins. All 8 stages capture their bits on the active clock edge.
2 SHIFT
Switch to SHIFT mode. Each clock edge moves the stored data by one stage toward the serial output.
3 OUTPUT
Read one bit per clock pulse. After 8 pulses, the full byte has been sent serially.
APPLICATIONS
Serial communication
Send data using fewer output wires.
Microcontrollers
Convert parallel sensor/data values to a serial stream.
Data transfer
Move bytes between digital subsystems.
Embedded systems
Useful where pin count or wiring is limited.
Key advantage: 8 parallel input lines are converted into a 1-bit-wide serial output.

## Slide 6
5. GitHub Repository
PROJECT FILES & EVIDENCE
Upload your Logisim circuit file (.circ), screenshots, and a short README so the project can be checked and reused.
RECOMMENDED REPOSITORY CONTENTS
8-bit-PISO-Register.circ
Logisim-demo.png
README.md (aim, design, truth/shift table)
REPOSITORY URL
Paste your GitHub link here
https://github.com/your-username/your-repo
QR PLACEHOLDER
Replace the sample URL and QR placeholder with your actual repository details before submission.
06